## Slide 1
Reducing Load Latency with Cache Level Prediction
——IEEE HPCA. 2022
汇报人：杨洁
Notes: XXXXXX
XXX

## Slide 2
01
02
03
04
Motivation
Design and Implementation
Evaluation
Conclusion
CONTENTS

## Slide 3
1
Motivation

## Slide 4
Three-level Cache Architecture
Good locality:
The number of demand load misses decreases
Evaluation
Design and Implementation
Conclusion
Motivation
1.1 Background
Bad locality:
Unnecessary lookup delays
Higher load latencies

## Slide 5
The Effectiveness of Lookup Strategy
Outside the red box
A good fit for sequential level lookup
Not benefit from level prediction
Evaluation
Design and Implementation
Conclusion
Motivation
1.1 Background
Inside the green box
Significant latency reductions from non-sequential lookup
Between the boxes
Modest performance gains from level prediction

## Slide 6
Evaluation
Design and Implementation
Conclusion
Motivation
1.2 Prior Searches
01
Prefetcher
  Moving data between levels prior to the execution of load instructions
  Mitigating the latency impact
Advantages
  Access slow main memory frequently
  Low average accuracy
Disadvantages

## Slide 7
2
Design and Implementation

## Slide 8
Evaluation
Motivation
Conclusion
Design and Implementation
2.1 Predictor Design
  Excluding L1 as a prediction target
  Including L2 as a prediction target
Levels to predict
  Being area-efficient to provide benefits
  Small and lower power for predictor structures
Resource and power
  PC + Miss history
  Address + Miss history
  Miss-Map approach
Level Prediction Approach
  Prefetchers add "noise" to the hit/miss history
  Coordinating the prefetcher and level predictor
Impact of Prefecthers

## Slide 9
Evaluation
Motivation
Conclusion
Design and Implementation
2.2 Cache Level Predictor
  Miss-Map >> Location-Map
    Providing the location of each block
    2 bits of metadata per block (64B)
  In-cache table >> In-memory table
    A small & consistent table
    Caching in a small meta-data cache
  Adding Popular Levels Detector
    Solving metadata cache miss
    Three counters
Extending the Miss-Map

## Slide 10
Evaluation
Motivation
Conclusion
Design and Implementation
2.3 LocMap & Tracking
  Time: L1 cache miss or updated
  Address: LocMap Address = Base Address + Physical Address >>14
LocMap Access
  Updating Events:
    Demand cache fills, dirty evictions, and prefetch fills that are metadata cache hits.
  Other Events:
    Prefetch fills with metadata cache missing
    Frequent clean evictions
    Coherence-induced level change
LocMap Update

## Slide 11
Evaluation
Motivation
Conclusion
Design and Implementation
2.3 LocMap & Tracking
Too small
  High miss ratio
  Updating LocMap frequently
  Degrading prediction
Too high
  Can't maintain low access latency&energy
Metadata Cache Size
2KB metadata cache provides a reasonable tradeoff

## Slide 12
Evaluation
Motivation
Conclusion
Design and Implementation
2.3 Popular Levels Detector
  Metadata cache missing
Time of Prediction
  Hitting level counter + 1 and others -1
Strategy of Updating
  Single-way prediction:
    Topmost is picked only (counter > threshold).
  Multi-way prediction:
    Topmost and second highest counter are picked (sum pf two counter > threshold).
    Three counters are all included (sum pf two counter < threshold).
Strategy of Prediction

## Slide 13
Evaluation
Motivation
Conclusion
Design and Implementation
2.4 Misprediction Detection
01
One-way correct prediction
  Allocate MSHR (L1) & Send request to L2
  Allocate MSHR (L2) & Forward request to the LLC
  Check tag-store
  Respond to the request (LLC)
  Deallocate MSHR (L2) & Fill the block into L2
  Forward the block to L1

## Slide 14
Evaluation
Motivation
Conclusion
Design and Implementation
2.4 Misprediction Detection
01
One-way correct prediction
  Allocate MSHR (L1) & Send request to L2
  Allocate MSHR (L1) & Forward request to the LLC
  Check tag-store
  Indicate block is present in L2 & Send a new request to L2
  Forward the block to L1
  Deallocate MSHR (L2)

## Slide 15
Evaluation
Motivation
Conclusion
Design and Implementation
2.4 Misprediction Detection
01
One-way correct prediction
  Allocate MSHR (L1) & Send request to L2
  Allocate MSHR (L2) & Forward request to the LLC & directory
  Check tag-store
  Indicate block is present in DRAM & Send request to DRAM

## Slide 16
3
Evaluation

## Slide 17
Design and Implementation
Motivation
Conclusion
Evaluation
3.1 Prediction Accuracy
  High LocMap metadata cache miss rate >> Lower accuracies
  Stale LocMap information >> Mispredictions
    Aggressive prefetchers: More clean evictions without updating.
    Poor locality: Large cache fills missed in metadata cache.
  High accuracy of the PLD
    Clear cache-level usage pattern.
    Multi-way access to multiple levels in parallel

## Slide 18
Design and Implementation
Motivation
Conclusion
Evaluation
3.2 Cache Energy
1
LocMap + PLD predictor is substantially better than either TAGE variant.
2
The LP results in an average energy saving of 16%.
3
D2D also exhibits overheads and can only improve on the LP by 3% on average.

## Slide 19
Design and Implementation
Motivation
Conclusion
Evaluation
3.2 Cache Energy
1
Speedup correlates well with the level-prediction potential
2
LP nearly matches the speedup of Ideal and D2D.
3
Just skipping L2 offers > 5% speedup for many applications.

## Slide 20
4
Conclusion

## Slide 21
Design and Implementation
Motivation
Evaluation
Conclusion
4. Conclusion
1
Many graph analytics and scientific applications benchmarks can benefit from non-sequential lookup
2
An effective, yet low-cost level predictor that operates in each core on the L1 cache miss path substantially outperforms cache miss predictors
3
Level prediction eliminates many unnecessary miss lookups.

## Slide 22
Thanks for watching!!
Notes: XXXXXX
XXX